## Slide 1: Multi Processor and Embedded System Session 4
Course : COMP6153
Effective Period : September 2018

## Slide 2: Sub Topics
Multicore vs Multiprocessor system
Multi Processor System
UMA s NUMA Processor
Multi Processor Synchronization
Scheduling
Characteristics of Embedded System
Purpose of Embedded System
eCOS

## Slide 3: These slides have been adapted from: Stallings, W. (2011). Operating Systems: Internals and Design Principles. 8th. ISBN: 978-0-13-380591-8 Chapter 10, 13
Acknowledgement

## Slide 4
At the end of this lecture, students are able to:
LO1 : Describe different types of muliprocessors and the components of an embedded system
LO2: To relate the fundamental design to the current development of Operating System
LO3: Demonstrate different techniques of the design of the Multiprocessor System
Learning Objectives

## Slide 5: Multiprocessor vs Multicore
Multicore system
CPU with more than one core
Cores operate as separate processor within a single chip
Increase performance without raising the processor clock speed
Multiprocessor system
Have more than one CPU
Some machine combines two technologies, multicore and multiprocessor

## Slide 6: Multiple Processor System
(a) A shared-memory multiprocessor. (b) A message-passing multicomputer. (c) A wide area distributed system.

## Slide 7: Architecture
Multiprocessor Systems are classified according to the manner of associating CPUs and memory units
  Uniform memory access (UMA) architecture
    Previously called tightly coupled multiprocessor
    Also called symmetrical multiprocessor (SMP)
    Examples: Balance system and VAX 8800
  Nonuniform memory access (NUMA) architecture
    Examples: HP AlphaServer and IBMNUMA-Q
  No-remote-memory-access (NORMA) architecture
    Example: Hypercube system by Intel
    Is actually a distributed system

## Slide 8: UMA Multiprocessors with Bus-Based Architectures
Three bus-based multiprocessors. (a) Without caching. (b) With caching. (c) With caching and private memories.

## Slide 9: NUMA Architecture
Operating Systems, by Dhananjay Dhamdhere

## Slide 10: UMA vs. NUMA
Unified Memory Access (UMA)
  also known as Symmetric MultiProcessors (SMP)
Non-Unified Memory Access (NUMA)
SIMILARITIES
  single memory space
  pitfall: Compared between shared memory and distributed memory.
DIFFERENT
  access time
  # of processors
  bus vs. network implementation

## Slide 11: Classification of parallel system
SISD (Single Instruction Single Data)
  Uniprocessors
MISD (Multiple Instruction Single Data)
  Stream based processing
SIMD (Single Instruction Multiple Data = DLP)
  Examples: Illiac-IV, CM-2 (Thinking Machines), Xetal (Philips), Imagine (Stanford), Vector machines, Cell architecture (Sony)
    Simple programming model
    Low overhead
MIMD (Multiple Instruction Multiple Data)
  Examples: Sun Enterprise 5000, Cray T3D, SGI Origin, Multi-core Pentiums, and many more….

## Slide 12: Classification of parallel system
SISD (Single Instruction Single Data)
  Uniprocessors
MISD (Multiple Instruction Single Data)
  Stream based processing
SIMD (Single Instruction Multiple Data = DLP)
  Examples: Illiac-IV, CM-2 (Thinking Machines), Xetal (Philips), Imagine (Stanford), Vector machines, Cell architecture (Sony)
    Simple programming model
    Low overhead
MIMD (Multiple Instruction Multiple Data)
  Examples: Sun Enterprise 5000, Cray T3D, SGI Origin, Multi-core Pentiums, and many more….

## Slide 13: Embedded System
Characteristics of Embedded System
Prpose of Embedded System
eCOS

## Slide 14: Embedded System
A combination of computer hardware and software, and designed to perform a dedicated function.
In many cases, embedded systems are part of a larger system or product, as in the case of an antilock braking system in a car

## Slide 15: Example of Embedded System

## Slide 16: Possible Organization of Embedded System

## Slide 17: Characteristics of Embedded System (1)
Real-time operation:
  In many embedded systems, the correctness of a computation depends, in part, on the time at which it is delivered. Often, real-time. Constraints are dictated by external I/O and control stability requirements.
Reactive operation:
  Embedded software may execute in response to external events. If these events do not occur periodically or at predictable intervals, the embedded software may need to take into account worst-case conditions and set priorities for execution of routines.

## Slide 18: Characteristics of Embedded System (2)
Configurability:
  Because of the large variety of embedded systems, there is a large variation in the requirements, both qualitative and quantitative, for embedded OS functionalityfor execution of routines.
I/O device flexibility:
  There is virtually no device that needs to be supported by all versions of the OS, and the range of I/O devices is large.
Streamlined protection mechanisms:
  Embedded systems are typically designed for a limited, well-defined functionality
Direct use of interrupts:
  General-purpose operating systems typically do not permit any user process to use interrupts directly

## Slide 19: Purpose Built Embedded Operating System
A significant number of operating systems have been designed from the ground up for embedded applications. Two prominent examples of this latter approach are eCos and TinyOS.

## Slide 20: Specialized Embedded System
Typically include
  Has a fast and lightweight process or thread switch
  Scheduling policy is real time and dispatcher module is part of scheduler instead of separate component.
  Has a small size
  Responds to external interrupts quickly; typical requirement is response time of less than 10 μs
  Minimizes intervals during which interrupts are disabled
  Provides fixed or variable-sized partitions for memory management as well as the ability to lock code and data in memory
  Provides special sequential files that can accumulate data at a fast rate To deal with timing constraints, the kernel provides bounded execution time for most primitives
  Maintains a real-time clock

## Slide 21: eCos
eCOS – Embedded Configurable Operating System
Open Source, royalty free, real time O/S for embedded application

## Slide 22: Configurability
eCos configuration tool, which runs on Windows or Linux, is used to configure an eCos package to run on a target embedded system
eCos package is structured hierarchically

## Slide 23: Loading eCos COnfiguration

## Slide 24: eCos Component
HAL – Harwarde Abstraction Layer
  HAL is software that presents a consistent API to the upper layers and maps upper-layer operations onto a specific hardware platform
eCos Kernel
  Designed to meet the following objectives:
    Low interrupt latency: The time it takes to respond to an interrupt and begin executing an ISR.
    Low task switching latency: The time it takes from when a thread becomes available to when actual execution begins.
    Small memory footprint: Memory resources for both program and data are kept to a minimum by allowing all components to configure memory as needed.
    Deterministic behavior: Throughout all aspect of execution, the kernels performance must be predictable and bounded to meet real-time application requirements.

## Slide 25: eCos Scheduler
Bitmap Sheduler
  A bitmap scheduler supports multiple priority levels, but only one thread can exist at each priority level at any given time.
Multilevel Queue Scheduler
  Supports up to 32 priority levels
  allows for multiple active threads at each priority level, limited only by system resources

## Slide 26
Stallings, W. (2014). Operating Systems: Internals and Design Principles. 8th. ISBN: 978-0-13-380591-8
www.yolinux.com
References