## Slide 1: Session 02 Network Model
Subject : Z1451 / Jaringan Komputer Year : 2015

## Slide 2: References
Main Reference Session 02: Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill Chapter 2.1; 2.2; 2.3

## Slide 3: Outline
Layering model
Model OSI 7 layer
Model TCP/IP

## Slide 4
2-1 PROTOCOL LAYERS
In Chapter 1, we discussed that a protocol is required when two entities need to communicate. When communication is not simple, we may divide the complex task of communication into several layers. In this case, we may need several protocols, one for each layer.
Let us use a scenario in communication in which the role of protocol layering may be better understood. We use two examples. In the first example, communication is so simple that it can occur in only one layer.
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
LAYERING MODEL

## Slide 5
Assume Maria and Ann are neighbors with a lot of common ideas. However, Maria speaks only Spanish, and Ann speaks only English. Since both have learned the sign language in their childhood, they enjoy meeting in a cafe a couple of days per week and exchange their ideas using signs. Occasionally, they also use a bilingual dictionary. Communication is face to face and Happens in one layer as shown in Figure 2.1.
Example 2.1
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
LAYERING MODEL

## Slide 6
Figure 2.1 Example 2.1
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
LAYERING MODEL

## Slide 7
Now assume that Ann has to move to another town because of her job. Before she moves, the two meet for the last time in the same cafe. Although both are sad, Maria surprises Ann when she opens a packet that contains two small machines. The first machine can scan and transform a letter in English to a secret code or vice versa. The other machine can scan and translate a letter in Spanish to the same secret code or vice versa. Ann takes the first machine; Maria keeps the second one. The two friends can still communicate using the secret code, as shown in Figure 2.2.
Example 2.2
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
LAYERING MODEL

## Slide 8
Figure 2.2 Example 2.2
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
LAYERING MODEL

## Slide 9
2-2 THE OSI MODEL
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. Almost three-fourths of countries in the world are represented in the ISO. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
MODEL OSI 7 LAYER

## Slide 10
ISO is the organization;
OSI is the model.
Note
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
MODEL OSI 7 LAYER

## Slide 11
Figure 2.3 The OSI model
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
MODEL OSI 7 LAYER

## Slide 12
Figure 2.4 OSI layers
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
MODEL OSI 7 LAYER

## Slide 13
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
MODEL OSI 7 LAYER

## Slide 14
2-3 TCP/IP PROTOCOL SUITE
The TCP/IP protocol suite was developed prior to the OSI model. Therefore, the layers in the TCP/IP protocol suite do not match exactly with those in the OSI model. The original TCP/IP protocol suite was defined as four software layers built upon the hardware. Today, however, TCP/IP is thought of as a five-layer model with the layers named similarly to the ones in the OSI model. Figure 2.7 shows both configurations.
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
NETWORK MODEL

## Slide 15
Comparison between OSI and TCP/IP
Layers in the TCP/IP Suite
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
MODEL OSI & TCP/IP LAYER

## Slide 16
Figure 2.7 Layers in the TCP/IP Protocol Suite
MODEL OSI & TCP/IP LAYER

## Slide 17
Figure 2.8 TCP/IP and OSI model
Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill
MODEL OSI & TCP/IP LAYER