## Slide 1: Session 04 Intranet
Subject : Z1451 / Jaringan Komputer Year : 2015

## Slide 2: References
Main Reference Session 05: Forouzan, B.A., (2010). Data Communications and Networking, 4th Edition, Mc.Graw-Hill Chapter 13 Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill Chapter 3.1

## Slide 3: Learning Outcomes
The students will be able to explain and use local area networks.

## Slide 4: Outline
Topology
Protocol Architecture
Hub, Switch
NIC

## Slide 5: LAN Topologies

## Slide 6
Categories of Standard Ethernet
Forouzan, B.A., (2010). Data Communications and Networking,4th Edition, Mc.Graw-Hill,Chapter 13

## Slide 7: Bus and Tree
Multipoint medium
Transmission propagates throughout medium
Heard by all stations
  Need to identify target station
    Each station has unique address
Need to regulate transmission
  To avoid collisions
  To avoid hogging
    Data in small blocks - frames

## Slide 8: Star Topology
Each station connected directly to central node
  Usually via two point to point links
Central node can broadcast
  Physical star, logical bus
  Only one station can transmit at a time
Central node can act as frame switch

## Slide 9: Shared Medium and Hub

## Slide 10: Bus and Hub
Bus configuration
  All stations share capacity of bus (e.g. 10Mbps)
  Only one station transmitting at a time
Hub uses star wiring to attach stations to hub
  Transmission from any station received by hub and retransmitted on all outgoing lines
  Only one station can transmit at a time
  Total capacity of LAN is 10 Mbps

## Slide 11: Two Level Star Topology

## Slide 12: Hub and Layer 2 Switch

## Slide 13: Layer 2 Switch Benefits
No change to attached devices to convert bus LAN or hub LAN to switched LAN
For Ethernet LAN, each device uses Ethernet MAC protocol
Device has dedicated capacity equal to original LAN
Layer 2 switch scales easily
  Additional devices attached to switch by increasing capacity of layer 2

## Slide 14: Protocol Architecture
Lower layers of OSI model
IEEE 802 reference model
Physical - UTP
Logical link control (LLC)
Media access control (MAC)

## Slide 15: LAN Standards
Created by the IEEE (Institute of Electrical and Electronics Engineers)
IEEE is a professional organization
  802 LAN MAN Standards Committee
    802.3 Working Group (Ethernet)
    Other working groups for other technologies
  Working groups create standards
Follow the OSI architecture

## Slide 16: Network Interface Card
NIC (Network Interface Card)
  Connect your computer with network
  Provide MAC addresses to each connection
  Implement CSMA/CD algorithm Provides ports for network connection.
When selecting a network card, consider:
  Type of network (Ethernet)
  Type of media (Twisted-pair, Fiber-optic)
  Type of system bus (PCI, ISA)

## Slide 17: NIC Functions
Logical link control (LLC):
  Communicates with upper layers in the computer
Naming:
  Provides a unique MAC address identifier
Framing:
  Part of the encapsulation process, packaging the bits for transport.

## Slide 18: NIC Functions
Media Access Control (MAC):
  Provides structured access to shared access media
Signaling:
  Creates signals and interface with the media