## Slide 1: Session 05 Addressing
Subject : Z1451 / Jaringan Komputer Year : 2015

## Slide 2: References
Main Reference Session 06: Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill Chapter 2.4, 5 Forouzan, B.A., (2010). Data Communications and Networking, 4th Edition, Mc.Graw-Hill Chapter 19

## Slide 3: Learning Outcomes
The students will be able to explain and use addressing scheme.

## Slide 4: Outline
Physical Address
Logical Addess
Application Access
DHCP

## Slide 5
Addresses in TCP/IP

## Slide 6: Physical Address
MAC Addresses are split in two:
  1st Half is the OUI
  2nd Half is Vendor Assigned
Format: oktet
44-AB-5F-DF-C1-FB

## Slide 7
IP Address
  A logical address used in TCP/IP networking for identifying a host in the network
IP Address Characteristics
  An IP address is 32 bits in size, unique, grouped into four 8-bit octets
  Octets are separated by decimal points
Network Administrator
  IP addresses are assigned by a network administrator according to an organization’s valid IP address range.
ICANN (Internet Corporation for Assigned Names & Numbers)
  Central authority on Internet addresses and names.
  A group of IP addresses must be obtained via an ISP.
Logical Address - IP Address

## Slide 8
Classful Addresses

## Slide 9
Some IP address numbers are reserved for special functions.
IP address whose numeric value is the highest value in the network (host bits all equal to one) is a broadcast address.
IP addresses with first octet of 127 such as 127.0.0.1 is a loopback IP used to test local workstation communication
IP addresses ending in “1” are typically reserved for gateway.
Special IP Addresses

## Slide 10
Private Addresses
A number of blocks in each class are assigned for private use. They are not recognized globally
Several techniques exist to hide internal network IP addresses from outside view
Any organization can use these addresses provide they adhere to the rules
All connectivity to an Internet host must be provided by a Network Address Translator

## Slide 11
Reserved IANA IP addresses for Private Internets
  10.0.0.0 - 10.255.255.255
    A single Class A network
  172.16.0.0 - 172.31.255.255
    Sixteen continuous Class B Networks
  192.168.0.0 - 192.168.255.255
    256 contiguous Class C networks
  Private IP Addresses

## Slide 12: Subnetting
Subnetting
Allows the use one class of addresses for several network segments
A subnetted address is comprised of three parts
  Network address
  Subnet address
  Host address
Subnet address uses part of the host address for subnet address assignment
Efficient use of IP addresses

## Slide 13: Subnetting
A subnet mask is a special bit pattern that blocks off the network portion of an IP address with an all-ones pattern
This activity of stealing bits from the host portion of further subdivide the network portion of an address is called subnetting a network address, or subnetting.
A subnet mask that is larger than the default mask for the address in use divides a single network IP address into multiple subnetworks

## Slide 14
Default mask and subnet mask

## Slide 15: Subnetting
First 2 octets represent part of extended network prefix.
3rd octet represents subnet.
4th octet represents host/machine/device.
Router needed to interpret addresses.
IP ending in “1” always reserved for gateways address.

## Slide 16: Application Addressing
Target user specified by User identification called socket in TCP/IP
  Transport entity identification
    Generally only one per host
    If more than one, then usually one of each type
      Specify transport protocol (TCP, UDP)
  Host address
    An attached network device
    In an internet, a global internet address

## Slide 17
Table 16.2 Options for DHCP
DHCP

## Slide 18
DHCP