## Slide 1: Session 08 Internetworking
Subject : Z1451 / Jaringan Komputer Year : 2015

## Slide 2: References
Main Reference Session 06: Forouzan, B.A., (2010). TCP/IP Protocol Suite, 4th Edition, Mc.Graw-Hill Chapter 3.5, 4, 7 Forouzan, B.A., (2010). Data Communications and Networking, 4th Edition, Mc.Graw-Hill Chapter 15, 20

## Slide 3: Learning Outcomes
The students will be able to explain internetworking principles

## Slide 4: Outline
Routing Principles
Devices:
  Router
  Switch

## Slide 5: Routing
Routing is the process of deciding what path to take from sender to receiver (packet forwarding)
Usually there is more than one route possible; devices that perform routing must keep tables to make decisions about which path to send packets on to reach a given destination (routing table)
Routing decisions on the Internet are usually handled by special purpose devices called Routers, that maintain their own routing tables
End systems and routers maintain routing tables
Routing table indicates next router to which datagram should be sent

## Slide 6: Routing
Data delivery from one computer to another is accomplished through store-and-forward technology
Packet switch stores incoming packet and forwards the packet to another switch or computer
Packet switch has internal memory, can hold packet if outgoing connection is busy (queued)

## Slide 7: Types of Routing
Centralized routing:
  Routing decisions are made by one central computer. Centralized routing can be found on small, mainframe-based networks.
Distributed (decentralized routing)
  Routing decisions are made independently at each routing node, although routers do exchange information).
  Two types:
      Static routing
      Dynamic routing

## Slide 8: Routing Strategies
Fixed
Flooding
Random
Adaptive

## Slide 9: Internetworking Terms
End System (ES)
  Device attached to one of the networks of an internet.
  Supports end-user applications or services.
Intermediate System (IS)
  Device used to connect two networks.
  Permits communication between end systems attached to different networks.

## Slide 10: Internetworking Devices
Types of devices for interconnecting LAN
        Routers
        Layer 2 switch
        Layer 3 switch

## Slide 11: Router
Complex large LANs need alternative routes
  Load balancing
  Fault tolerance
Routing selected for each source-destination pair.
Routers do all IP-level processing in software.
High-speed LANs and high-performance layer 2 switches pump millions of packets per second.
Layer 3 switches
  Implementpacket-forwarding logic of router in hardware
Two categories:
  Packet by packet
  Flow base

## Slide 12: Layer 3 Switch
Packet by Packet
  Operates the same way as traditional router
  Order of magnitude increase in performance
Flow-based switch
  Tries to enhance performance by identifying flows of IP packets of same source and destination
  Done by observing ongoing traffic
  Once flow is identified, predefined route can be established